## Slide 1
Memory-Based Rack Area Networking
Presented by: Cheng-Chun Tu
Advisor: Tzi-cker Chiueh
Stony Brook University & Industrial Technology Research Institute

## Slide 2: Disaggregated Rack Architecture
Rack becomes a basic building block for cloud-scale data centers
CPU/memory/NICs/Disks embedded in self-contained server
  Disk pooling in a rack
  NIC/Disk/GPU pooling in a rack
  Memory/NIC/Disk pooling in a rack
Rack disaggregation
  Pooling of HW resources for global allocation and independent upgrade cycle for each resource type
Notes: Hyperscale data centers increasingly use a rack rather than a machine as the basic building block.
A disaggregated rack architecture, in which a rack consists of a CPU/memory pool, a disk pool, and a network interface (NIC) pool, which are connected through a high-bandwidth and low-latency rack-area network.
Operationally, a major advantage of the disaggregated rack architecture is that it allows different system components, i.e. CPU, memory, disk and NIC, to be upgraded according to their own technology cycle.

## Slide 3: Requirements
High-Speed Network
I/O Device Sharing
Direct I/O Access from VM
High Availability
Compatible with existing technologies
Notes: The enabling technology or the requirements for disaggregated rack architecture includes
The key enabling technology for the disaggregated rack architecture is a High-speed rack-area networking that allows direct memory access
Today every server has an on-board PCIe bus
We propos a hybrid TOR switch that consists of both PCIe port and Ethernet ports

## Slide 4
Reduce cost: One I/O device per rack rather than one per host
Maximize Utilization: Statistical multiplexing benefit
Power efficient: Intra-rack networking and device count
Reliability: Pool of devices available for backup
Operating Sys.
App1
App2
Non-Virtualized
Host
Hypervisor
VM1
VM2
Virtualized Host
Operating Sys.
App1
App2
Non-Virtualized
Host
Hypervisor
VM1
VM2
Virtualized Host
Switch
10Gb Ethernet / InfiniBand switch
Co-processors
HDD/Flash-Based RAIDs
Ethernet NICs
Shared Devices:
GPU
SAS controller
Network Device
… other I/O devices
I/O Device Sharing
Notes: From the architectural standpoint, rack disaggregation decouples CPU/memory from I/O devices such as disk controllers and network interfaces,
and enables more efficient, flexible and robust I/O resource sharing.
The figure below shows the idea of I/O disaggregation,
We have non-virtualized host which runs the traditional OS, and virtualized host with multiple virtual machines
Each server extend their PCIe bus from its motherboard into a PCIe switch using PCIe expansion card.
Instead of using Ethernet switch, the PCIe switch becomes the new ToR switch, which requires to support intra-rack communication, the communication between servers
And the inter-rack communication, the communication out of the rack.
The benefits of I/O device disaggregation include
Reduce cost: because the I/O devices are shared in a rack so
And by leveraging the statistical multiplexing, each device can be full utilized, no device is idling
Power efficient: PCIe is more power-efficient because its transceiver is designed for short distance connectivity and thus is simpler and consumes less power.
Reliability:

## Slide 5: PCI Express
PCI Express is a promising candidate
  Gen3 x 16 lane = 128Gbps with low latency (150ns per hop)
  New hybrid top-of-rack (TOR) switch consists of PCIe ports and Ethernet ports
Universal interface for I/O Devices
  Network , storage, graphic cards, etc.
  Native support for I/O device sharing
I/O Virtualization
  SR-IOV enables direct I/O device access from VM
  Multi-Root I/O Virtualization (MRIOV)

## Slide 6: Challenges
Single Host (Single-Root) Model
  Not designed for interconnecting/sharing amount multiple hosts (Multi-Root)
Share I/O devices securely and efficiently
Support socket-based applications over PCIe
Direct I/O device access from guest OSes

## Slide 7: Observations
PCIe: a packet-based network (TLP)
  But all about it is memory addresses
Basic I/O Device Access Model
  Device Probing
  Device-Specific Configuration
  DMA (Direct Memory Access)
  Interrupt (MSI, MSI-X)
Everything is through memory access!
  Thus, “Memory-Based” Rack Area Networking

## Slide 8: Proposal: Marlin
Unify rack area network using PCIe
  Extend server’s internal PCIe bus to the TOR PCIe switch
  Provide efficient inter-host communication over PCIe
Enable clever ways of resource sharing
  Share network, storage device, and memory
Support for I/O Virtualization
  Reduce context switching overhead caused by interrupts
Global shared memory network
  Non-cache coherent, enable global communication through direct load/store operation

## Slide 9: Introduction
PCIe Architecture, SR-IOV, MR-IOV, and NTB (Non-Transparent Bridge)

## Slide 10: PCIe Single Root Architecture
CPU #n
PCIe
Root Complex
PCIe
Endpoint
PCIe TB
Switch
PCIe
Endpoint
PCIe TB
Switch
PCIe TB
Switch
PCIe
Endpoint3
PCIe
Endpoint1
PCIe
Endpoint2
CPU #n
CPU #n
Multi-CPU, one root complex hierarchies
  Single PCIe hierarchy
Single Address/ID Domain
  BIOS/System software probes topology
  Partition and allocate resources
Each device owns a range(s)of physical address
  BAR addresses, MSI-X, and device ID
  Strict hierarchical routing
TB: Transparent Bridge
Routing table BAR:
0x10000 – 0x90000
Routing table BAR:
0x10000 – 0x60000
BAR0: 0x50000 - 0x60000
Write Physical Address:
0x55,000
To Endpoint1
Notes: So what is Single root?
The PCIe hierarchy in Today’s server is a single root architecture.
Multiple CPUs are connected to the root complex.
And the process of PCI enumeration starts probing from the root complex,
To all the devices on the board and assigned BAR addresses to each endpoints and device ID as well as routing information to to transparent bridges.
So this is a single address space domain, with each device owns some resources

## Slide 11: Single Host I/O Virtualization
Direct communication:
  Direct assigned to VMs
  Hypervisor bypassing
Physical Function (PF):
  Configure and manage the SR-IOV functionality
Virtual Function (VF):
  Lightweight PCIe function
  With resources necessary for data movement
Intel VT-x and VT-d
  CPU/Chipset support for VMs and devices
Figure: Intel® 82599 SR-IOV Driver Companion Guide
Makes one device “look” like multiple devices
VF
VF
VF
Can we extend virtual NICs to multiple hosts?
Host1 Host2 Host3
Notes: IOV vritualizaion make one physical device look like many devices
The most common example is the network card in a physical machine running multiple VMs.
Without IOV, the hypervisor needs to have an software switch that copies receiving packet and transmitting packets to and from the physical NIC.
This greatly increases the CPU’s workload and decreases the overall IO performance.
With IO virtualization, multiple virtual devices (we called VF, virtual function or Virtual NIC) can be configured in one device.
And directly pass through to the VM.
So each VM works as it has the network interface card and the packet transmission and reception no longer involve hypervisor.
The software model of SRIOV includes a PF and multiple VF
The virtual NIC or virtual function is a light weight PCIe function with resource for data plane.
However, today’ IOV is restricted in a single host or single root. The other hosts, or other VM on other hosts can not share the resources.
===
Single root IOV pushes much of the SW overhead into the IO adapter
Leads to improve performance for guest OS applications
http://www.istockanalyst.com/finance/story/6239562/intel-intc-facebook-fb-collaborating-on-new-rack-scale-server-architecture

## Slide 12: Multi-Root Architecture
Interconnect multiple hosts
  No coordination between RCs
  One domain for each root complex  Virtual Hierarchy (VH)
  Endpoint4 is shared
Multi-Root Aware (MRA) switch/endpoints
  New switch silicon
  New endpoint silicon
  Management model
  Lots of HW upgrades
  Not/rare available
CPU #n
PCIe Root Complex1
CPU #n
CPU #n
PCIe MR
Endpoint3
PCIe MRA Switch1
PCIe TB
Switch3
PCIe TB
Switch2
PCIe MR
Endpoint6
PCIe MR
Endpoint4
PCIe MR
Endpoint5
PCIe
Endpoint1
PCIe
Endpoint2
CPU #n
PCIe Root Complex2
CPU #n
CPU #n
CPU #n
PCIe Root Complex3
CPU #n
CPU #n
Host Domains
Shared Device Domains
MR PCIM
Link
VH1
VH2
VH3
Shared by
VH1 and VH2
How do we enable MR-IOV without relying
on Virtual Hierarchy?
Host1 Host2 Host3
Notes: As for multi root, multiple host domains can be connected together using PCIe cable with an enhanced PCIe switch in the middle , or the MR-capable PCIe switch
Each single host domain still has its local endpoint and address space, and it is also allowed to access the shared device pool under the enhanced PCIe switch.
So the main task of the enhanced pcie switch is to isolate each host domain’s address space and provide mechanism for
CPUs in different domains to access the shared device or the other way around.
Obviously, this is much harder than SRIOV, because it require not only the enhanced PCIe switch, but all external IO devices need to support MR IOV.
It requires new switch silicon, endpoints and management model.
Our solution is to use NTB to isolation between host domains as well as provide data communication.
== End ==
  VH (Virtual Hierarchy)
map the virtual functions to the assigned host domain, and route the PCIe transcation to the destionation.

## Slide 13: Non-Transparent Bridge (NTB)
Isolation of two hosts’ PCIe domains
  Two-side device
  Host stops PCI enumeration
  at NTB-D.
  Yet allow status and data exchange
Translation between domains
  PCI device ID:
  Querying the ID lookup table (LUT)
  Address:
  From primary side and secondary side
Example:
  External NTB device
  CPU-integrated: Intel Xeon E5
Figure: Multi-Host System and Intelligent I/O Design with PCI Express
[1:0.1]
Host A
Host B
[2:0.2]
Notes: NTB is a PCI-SIG standard which defines is a device having sides back-to-back that isolates two PCIe domain.
As shown in the right figure, we connect two servers, A and B, using NTB.
Host A on top initially do device enumeration, found endpoint X and stops enumerating at NTB,
While host B below detects endpoints Y, and stops at the lower side of the NTB.
So both the host A and host B has their independent address spaces, and
NTB provide 2 translation mechanisms: The ID translation and The address translation
The ID translation allows a device in a domain to be accessed by the other domain by looking up an ID translation table called “LUT” (look up table)
For example, endpoint X could be assigned ID 1:0.1, and the host B can access it using 2:0.0 by looking up the translation table.
The address translation allows the PCIe memory read /write to cross the NTB and reach the other address domain.
===
Multi-Host System and Intelligent I/O Design with PCI Express
The non-transparent bridging (NTB) function enables isolation of two hosts or memory domains yet allows status and data exchange between the two hosts or sub-systems.

## Slide 14: NTB Address Translation
NTB address translation:
  <the primary side to the secondary side>
Configuration:
  addrA at primary side’s BAR window to addrB at the secondary side
Example:
  addrA = 0x8000 at BAR4 from HostA
  addrB = 0x10000 at HostB’s DRAM
One-way Translation:
  HostA read/write at addrA (0x8000) == read/write addrB
  HostB read/write at addrB has nothing to do with addrA in HostA
Figure: Multi-Host System and Intelligent I/O Design with PCI Express
Notes: Let’s take an example of address translation.
We have hostA on the left side and host B on the right side.
If host A want to access the memory region of host B,
We first open an address window on address 0x8000 at host A and set up the translation register to target the address 0x10000 at the hostB.
By this configuration, when hostA’s CPU or device writes or read address 0x8000,
the PCIe packet containing this address will be translated to address 0x10000 in hostB’s domain and write to this memory location.

## Slide 15: I/O Device Sharing
Sharing SR-IOV NIC securely and efficiently [ISCA’13]

## Slide 16: Global Physical Address Space
0
Physical Address Space of MH
248 = 256T
VF1
VF2
:
VFn
MMIO
Physical Memory
CH1
MMIO
Physical Memory
MH
CSR/MMIO
MMIO
Physical Memory
CH n
MMIO
Physical Memory
CH2
NTB
NTB
IOMMU
IOMMU
NTB
IOMMU
Leverage unused physical address space, map each host to MH
Each machine could write to another machine’s entire physical address space
128G
192G
256G
64G
Local
< 64G
Global
> 64G
MH writes
to 200G
CH writes
To 100G
MH: Management Host
CH: Compute Host
Notes: Of course, this accessibility is carefully regulated through various mapping tables, specifically, EPT, IOMMU and device ID table.

## Slide 17
CH’s Physical Address Space
CPU
PT
NTB
IOMMU
5. MH’s CPU
Write 200G
hpa
hva
dva
CPU
GPT
EPT
4. CH VM’s CPU
gva
gpa
CPU
PT
DEV
IOMMU
CH’s CPU
CH’s device
dva
hva
-> host physical addr.
-> host virtual addr.
-> guest virtual addr.
-> guest physical addr.
-> device virtual addr.
hpa
hva
dva
gva
gpa
NTB
IOMMU
DEV
IOMMU
6. MH’s device
(P2P)
dva
dva
hpa
Address Translations
CPUs and devices could access remote host’s memory address space directly.

## Slide 18: Virtual NIC Configuration
4 Operations: CSR, device configuration, Interrupt, and DMA
Observation: everything is memory read/write!
Sharing: a virtual NIC is backed by a VF of an SRIOV NIC and redirect memory access cross PCIe domain
Native I/O device sharing is realized by
memory address redirection!

## Slide 19: System Components
Management Host (MH)
Compute Host (CH)

## Slide 20: Parallel and Scalable Storage Sharing
Proxy-Based Non-SRIOV SAS controller
  Each CH has a pseudo SCSI driver to redirect cmd to MH
  MH has a proxy driver receiving the requests, and enable SAS controller to direct DMA and interrupt to CHs
Two direct accesses out of 4 Operations:
  Redirect CSR and device configuration: involve MH’s CPU.
  DMA and Interrupts are directly forwarded to the CHs.
Pseudo SAS driver
SAS Device
Proxy-Based SAS driver
SCSI cmd
DMA and Interrupt
Compute Host1
Management
Host
iSCSI initiator
Compute Host2
TCP(iSCSI)
TCP(data)
Ethernet
PCIe
SAS Device
iSCSI Target
Management
Host
SAS driver
DMA and Interrupt
Marlin
iSCSI
Bottleneck!
See also: A3CUBE’s Ronnie Express

## Slide 21: Security Guarantees: 4 cases
PF
VF1
SR – IOV Device
PF
Main Memory
MH
VM1
VM2
VF
VF
CH1
VMM
VM1
VM2
VF
VF
CH2
VMM
VF2
VF3
VF4
Device assignment
Unauthorized Access
PCIe Switch Fabric
VF1 is assigned to VM1 in CH1, but it can screw multiple memory areas.

## Slide 22: Security Guarantees
Intra-Host
  A VF assigned to a VM can only access to memory assigned to the VM. Accessing other VMs is blocked host’s IOMMU
Inter-Host:
  A VF can only access the CH it belongs to. Accessing other hosts is blocked by other CH’s IOMMU
Inter-VF / inter-device
  A VF can not write to other VF’s registers.
  Isolate by MH’s IOMMU.
Compromised CH
  Not allow to touch other CH’s memory nor MH
  Blocked by other CH/MH’s IOMMU
Global address space for resource sharing is secure and efficient!

## Slide 23: Inter-Host Communication
Topic: Marlin Top-of-Rack Switch, Ether Over PCIe (EOP)
CMMC (Cross Machine Memory Copying), High Availability

## Slide 24: Marlin TOR switch
Each host has 2 interfaces: inter-rack and inter-host
Inter-Rack traffic goes through Ethernet SRIOV device
Intra-Rack (Inter-Host) traffic goes through PCIe
Ethernet
PCIe

## Slide 25: Inter-Host Communication
HRDMA: Hardware-based Remote DMA
  Move data from one host’s memory to another host’s memory using the DMA engine in each CH
How to support socket-based application?
  Ethernet over PCIe (EOP)
  An pseudo Ethernet interface for socket applications
How to have app-to-app zero copying?
  Cross-Machine Memory Copying (CMMC)
  From the address space of one process on one host to the address space of another process on another host
Notes: Intel quickdata dma

## Slide 26: Cross Machine Memory Copying
Device Support RDMA
  Several DMA transactions, protocol overhead, and device-specific optimization.
Native PCIe RDMA, Cut-Through forwarding
CPU load/store operations (non-coherent)
InfiniBand/Ethernet RDMA
DMA to internal
device memory
Payload
fragmentation/encapsulation,
DMA to the IB link
RX buffer
DMA to receiver buffer
PCIe
Payload
RX buffer
PCIe
DMA engine
(ex: Intel Xeon E5 DMA)
IB/Ethernet

## Slide 27: Inter-Host Inter-Processor INT
I/O Device generates interrupt
Inter-host Inter-Processor Interrupt
  Do not use NTB’s doorbell due to high latency
  CH1 issues 1 memory write, translated to become an MSI at CH2 (total: 1.2 us latency)
InfiniBand/Ethernet
Send packet
IRQ handler
Interrupt
PCIe Fabric
Data / MSI
IRQ handler
Interrupt
Memory Write
NTB
CH1 Addr: 96G+0xfee00000
CH2 Addr: 0xfee00000
CH1
CH2

## Slide 28: Shared Memory Abstraction
Two machines share one global memory
  Non-Cache-Coherent, no LOCK# due to PCIe
  Implement software lock using Lamport’s Bakery Algo.
Dedicated memory to a host
Reference: Disaggregated Memory for Expansion and Sharing in Blade Servers [ISCA’09]
Remote
Memory
Blade
PCIe fabric
Compute
Hosts

## Slide 29: Control Plane Failover
Virtual Switch 1
Ethernet
upstream
…
…
Slave MH
…
Master MH
VS2
Virtual Switch 2
Ethernet
TB
…
…
…
VS1
Slave MH
Master MH
  MMH (Master) connected to the upstream port of VS1, and
  BMH (Backup) connected to the upstream port of VS2.
  When MMH fails, VS2 takes over all the downstream ports
  by issuing port re-assignment (does not affect peer-to-peer routing states).

## Slide 30: Multi-Path Configuration
0
Physical Address Space of MH
248
MMIO
Physical Memory
MH
MMIO
Physical Memory
CH1
Prim-NTB
Back-NTB
Equip two NTBs per host
  Prim-NTB and Back-NTB
  Two PCIe links to TOR switch
Map the backup path to backup address space
Detect failure by PCIe AER
  Require both MH and CHs
Switch path by remap virtual-to-physical address
Primary Path
Backup Path
128G
192G
1T+128G
MH writes to 200G goes through primary path
MH writes to 1T+200G goes through backup path
Notes: Of course, this accessibility is carefully regulated through various mapping tables, specifically, EPT, IOMMU and device ID table.

## Slide 31: Direct Interrupt Delivery
Topic: Direct SRIOV Interrupt,
Direct virtual device interrupt , Direct timer Interrupt

## Slide 32: DID: Motivation
4 operations: interrupt is not direct!
  Unnecessary VM exits
  Ex: 3 exits per Local APIC timer
Existing solutions:
  Focus on SRIOV and leverage shadow IDT (IBM ELI)
  Focus on PV, require guest kernel modification (IBM ELVIS)
  Hardware upgrade: Intel APIC-v or AMD VGIC
  DID direct delivers ALL interrupts without paravirtualization
Guest
(non-root mode)
Host
(root mode)
Timer
set-up
End-of-
Interrupt
Interrupt
Injection
Interrupt due
To Timer expires
Start handling the timer
Software Timer
Software Timer
Inject vINT

## Slide 33: Direct Interrupt Delivery
Definition:
  An interrupt destined for a VM
  goes directly to VM without any
  software intervention.
  Directly reach VM’s IDT.
Disable external interrupt exiting (EIE) bit in VMCS
Challenges: mis-delivery problem
  Delivering interrupt to the unintended VM
  Routing: which core is the VM runs on?
  Scheduled: Is the VM currently de-scheduled or not?
  Signaling completion of interrupt to the controller (direct EOI)
Hypervisor
VM
core
SRIOV
Back-end
Drivers
VM
core
Virtual device
Local APIC timer
SRIOV device
Virtual Devices

## Slide 34: Direct SRIOV Interrupt
Every external interrupt triggers VM exit, allowing KVM to inject virtual interrupt using emulated LAPIC
DID disables EIE (External Interrupt Exiting)
  Interrupt could directly reach VM’s IDT
How to force VM exit when disabling EIE? NMI
IOMMU
core1
VM1
IOMMU
core1
VM2
1. VM M is running.
2. Interrupt for VM M,
but VM M is de-scheduled.
SRIOV
VF1
NMI
1. VM Exit
2. KVM receives INT
3. Inject vINT
SRIOV
VF1
VM1

## Slide 35: Virtual Device Interrupt
Assume VM M has virtual device with vector #v
DID: Virtual device thread (back-end driver) issues IPI with vector #v to the CPU core running VM
The device’s handler in VM gets invoked directly
If VM M is de-scheduled, inject IPI-based virtual interrupt
core
VM (v)
core
I/O thread
Tradition: send IPI and
kick off the VM, hypervisor inject virtual interrupt v
core
VM (v)
core
I/O thread
DID: send IPI directly
with vector v
VM Exit
Assume device vector #: v

## Slide 36: Direct Timer Interrupt
DID direct delivers timer to VMs:
  Disable the timer-related MSR trapping in VMCS bitmap.
  Timer interrupt is not routed through IOMMU so when VM M runs on core C, M exclusively uses C’s LAPIC timer
  Hypervisor revokes the timers when M is de-scheduled.
LAPIC
IOMMU
CPU1
LAPIC
CPU2
Today:
  x86 timer is located in the per-core local APIC registers
  KVM virtualizes LAPIC timer to VM
    Software-emulated LAPIC.
  Drawback: high latency due to several VM exits per timer operation.
External
interrupt
timer

## Slide 37: DID Summary
DID direct delivers all sources of interrupts
  SRIOV, Virtual Device, and Timer
  Enable direct End-Of-Interrupt (EOI)
  No guest kernel modification
  More time spent in guest mode
SR-IOV
interrupt
Timer
interrupt
PV
interrupt
Guest
Host
SR-IOV
interrupt
time
EOI
EOI
EOI
EOI
Guest
Host

## Slide 38: Implementation & Evaluation

## Slide 39: Prototype Implementation
OS/hypervisor:
Fedora15 / KVM
Linux 2.6.38 / 3.6-rc4
CH:
Intel i7 3.4GHz /
Intel Xeon E5
8-core CPU
8 GB of memory
MH:
Supermicro E3 tower
8-core Intel Xeon 3.4GHz
8GB memory
VM:
Pin 1 core, 2GB RAM
NIC: Intel 82599
Link: Gen2 x8 (32Gb)
NTB/Switch:
PLX8619
PLX8696

## Slide 40
48-lane 12-port PEX 8748
NTB PEX 8717
Intel 82599
PLX Gen3 Test-bed
Intel NTB Servers
1U server behind

## Slide 41: Software Architecture of CH
MSI-X

## Slide 42: I/O Sharing Performance
Chart: Message Size (Kbytes)
| 64.0 | 32.0 | 16.0 | 8.0 | 4.0 | 2.0 | 1.0
SRIOV | 9.007 | 8.96 | 8.8943 | 6.1425 | 2.479 | 1.1448 | 0.569
MRIOV | 8.6 | 8.5 | 8.3933 | 6.1017 | 2.4388 | 1.1267 | 0.56675
MRIOV+ | 9 | 8.88 | 8.8943 | 6.15 | 2.479 | 1.1 | 0.569
Copying Overhead

## Slide 43: Inter-Host Communication
Chart: Message Size (Byte)
| 65536.0 | 32768.0 | 16384.0 | 8192.0 | 4096.0 | 2048.0 | 1024.0
TCP unaligned | 11 | 9.5 | 5.5 | 5 | 2 | 1 | 0.5
TCP aligned+copy | 19 | 18 | 17.9 | 15.3 | 9.8 | 4.8 | 2
TCP aligned | 19.6 | 19 | 17 | 15 | 11 | 6 | 2
UDP aligned | 19.9 | 19.02 | 17.982 | 15.954 | 11.433 | 6.182 | 2.992
TCP unaligned: Packet payload addresses are not 64B aligned
TCP aligned + copy: Allocate a buffer and copy the unaligned payload
TCP aligned: Packet payload addresses are 64B aligned
UDP aligned: Packet payload addresses are 64B aligned

## Slide 44
Setup: VM runs cyclictest, measuring the latency between
hardware interrupt generated and user level handler is invoked.
experiment: highest priority, 1K interrupts / sec
KVM shows 14us due to 3 exits: external interrupt, program x2APIC (TMICT), and EOI per interrupt handling.
KVM latency is much higher due to 3 VM exits
DID has 0.9us overhead
Interrupt Invocation Latency

## Slide 45: Memcached Benchmark
DID improve x3 performance
Set-up: twitter-like workload and measure the peak requests served per second (RPS) while maintaining 10ms latency
PV / PV-DID: Intra-host memecached client/sever
SRIOV/SRIOV-DID: Inter-host memecached client/sever
DID improves 18% TIG (Time In Guest)
TIG: % of time
CPU in guest mode
Notes: emulate a twitter-like workload and measure the peak requests served per second (RPS) while maintaining 10ms latency for at least 95% of requests.

## Slide 46: Discussion
Ethernet / InfiniBand
  Designed for longer distance, larger scale
  InfiniBand is limited source (only Mellanox and Intel)
QuickPath / HyperTransport
  Cache coherent inter-processor link
  Short distance, tightly integrated in a single system
NUMAlink / SCI (Scalable Coherent Interface)
  High-end shared memory supercomputer
PCIe is more power-efficient
  Transceiver is designed for short distance connectivity

## Slide 47: Contribution
We design, implement, and evaluate a PCIe-based rack area network
  PCIe-based global shared memory network using standard and commodity building blocks
  Secure I/O device sharing with native performance
  Hybrid TOR switch with inter-host communication
  High Availability control plane and data plane fail-over
  DID hypervisor: Low virtualization overhead
Marlin Platform
Processor Board
PCIe Switch Blade
I/O Device Pool

## Slide 48: Other Works/Publications
SDN
  Peregrine: An All-Layer-2 Container Computer Network, CLOUD’12
  SIMPLE-fying Middlebox Policy Enforcement Using SDN, SIGCOMM’13
  In-Band Control for an Ethernet-Based Software-Defined Network, SYSTOR’14
Rack Area Networking
  Secure I/O Device Sharing among Virtual Machines on Multiple Host, ISCA’13
  Software-Defined Memory-Based Rack Area Networking, under submission to ANCS’14
  A Comprehensive Implementation of Direct Interrupt,
  under submission to ASPLOS’14

## Slide 49: Thank You
Question?
Dislike? Like?

## Slide 50: PCIe Practical Issues
Signal Integrity
  High speed signals can deteriorate to unacceptable levels
  Around 10 meters
Retimers, repeaters, redrivers

## Slide 51: Requirements of NFV platform
Bare-metal hypervisor performance
  Especially I/O performance  DID hypervisor
Fast inter-VM or inter-network function channel
  PCIe fabric, global address space, HRDMA, device sharing
Enforce middlebox processing sequences
  Leverage the SDN controller and OpenFlow [SIMPLE-SIGCOMM’13]

## Slide 52: Future Work: Software-Defined NFV Platform

## Slide 53: Backup Materials

## Slide 54: System-Level Related Work
Proprietary hardware
  PLX FabricExpress (2013)
A3Cube Ronniee Express (March 2014)

## Slide 55: SDN and NFV
Software-Defined Network (SDN)
  Separate control and forwarding
  Centralized Controller
  Protocol to couple control and forwarding: OpenFlow
  Self-contained switch
Network Function Virtualization (NFV)
  Leverage commodity servers and switches,
  no dedicated appliances -> reduce CAPEX and OPEX
  Enable service innovation
Complimentary to each other

## Slide 56: Construction of Global Address Space
Example:
MH writes to 32GB
  CH1’s address 0, usually in DRAM.
MH writes to 64GB
  goes to CH2’s address 0
CH1 writes to 96GB
  MH writes to 64GB
  CH2’s address 0
Any memory address of any host in the rack is accessible
Notes: To support the three communication primitives,
We first need to construct a global memory pool or global memory address space, by allowing all hosts memory address space to be accessible from all other hosts
The construction requires two address translations;
one set up by the MH to map the physical memory of every attached machine to the MH’s physical memory address space, as shown in (a), and the other done by each attached machine to map the MH’s physical memory address space into its own local physical address space, as shown in (b).